Take-over time in highly automated vehicles: non-critical transitions to and from manual control

Alexander Eriksson, Neville A Stanton
Transportation Research Group, Faculty of Engineering and the Environment, University of Southampton, Boldrewood campus, SO16 7QF, UK

Running head: Take-over time in automated vehicles

Manuscript type: Research article

Word count: 4791

Corresponding author: Alexander Eriksson Transportation Research Group, Faculty of Engineering and the Environment, University of Southampton, Boldrewood campus, SO16 7QF, UK. Email: Alexander.eriksson@soton.ac.uk

Acknowledgements: This research has been conducted as a part of the European Marie Curie ITN project HFAuto - Human Factors of Automated driving (PITN-GA-2013-605817)

Biographies

Alexander Eriksson, MSc, received his Master of Science degree in Cognitive Science from Linköping University in 2014 and is currently a Marie Curie Research Fellow in the EU funded Marie Curie International Training Network on Human Factors in Highly Automated Vehicles (HF-Auto) within the Faculty of Engineering and the Environment at the University of Southampton where he is undertaking his PhD research. His primary research focus is on human-automation interaction, specifically in how automated vehicles hands back control to the driver in terms of information presentation and cues.

Professor Neville Stanton, PhD, DSc, is a Chartered Psychologist, Chartered Ergonomist and a Chartered Engineer and holds the Chair in Human Factors Engineering in the Faculty of Engineering and the Environment at the University of Southampton.  He is leading the EPSRC/JLR funded project on Human Interaction: Designing Automated Vehicles (HI:DAVe) and is a partner in the EU funded Marie Curie International Training Network on Human Factors in Highly Automated Vehicles (HF-Auto).

Abstract

Objective: The aim of this study was to review existing research into driver control transitions and to determine the time it takes drivers to resume control from a highly automated vehicle in non-critical scenarios. 
Background: Contemporary research has moved from an inclusive design approach to only adhering to mean/median values when designing control transitions in automated driving. Research into control transitions in highly automated driving has focused on urgent scenarios where drivers are given a relatively short time span to respond to a request to resume manual control. We found a paucity in research into more frequent scenarios for control transitions, such as planned exits from highway systems.
Method: Twenty six drivers drove two scenarios with an automated driving feature activated. Drivers were asked to read a newspaper, or to monitor the system, and to relinquish, or resume, control from the automation when prompted by vehicle systems.
Results: Significantly longer control transition times were found between driving with and without secondary tasks. Control transition times were substantially longer than those reported in the peer-reviewed literature.
Conclusion: We found that drivers take longer to resume control when under no time-pressure compared to that reported in the literature. Moreover, we found that drivers occupied by a secondary task exhibit larger variance, and slower responses to requests to resume control. Workload scores implied optimal workload.
Application: Intra- and inter-individual differences need to be accommodated by vehicle manufacturers and policy makes alike to ensure inclusive design of contemporary systems and safety during control transitions.

Keywords: Automation, Automated Driving, Control Transitions, Take-Over Requests, Driving Performance, Task Regulation

Précis: This study reviews the literature for non-critical control transitions in highly automated driving and contrasts the reported results with driver-paced control transitions. The results show increased response times compared to the literature, and when engaged in secondary tasks compared with no task engagement. The study also reports on transition times from manual to automated driving for the first time.

Topic Choice:  Surface Transportation

Introduction

Highly automated vehicles are becoming an engineering reality and will become commonplace on our roads in the very near future (Walker et al., 2015). For example, Tesla released its Autopilot feature in 2015, with BMW, Mercedes and Audi quickly following with similar technologies (Audi, 2014; BMW, 2013; safecarnews.com, 2015). It is a common misconception that these features are ‘highly automated’ when they are in fact classified as conditional driving automation (SAE Level 3, 'SAE International, 2016). This means that they come with limitations, such as the features may only be intended for use under certain Operational Design Domains, for example, on highways, as well as requiring driver monitoring and intervention (Stanton et al., 1997; Wolterink et al., 2011).

When using a driver assistance system that is able to automate the driving task to such an extent that hands- and feet-free driving is possible (SAE Level 3, 'SAE International, 2016), the driver becomes decoupled from the operational and tactical levels of control (Michon, 1985; Stanton & Young, 2005), leaving the high level strategic goals to be dealt with by the driver (until the point of resuming manual control). This is a form of “driver-initiated automation”, where the driver is in control of when the system becomes engaged or disengaged (Banks & Stanton, 2015, 2016; Lu & de Winter, 2015). Indeed, according to Bainbridge (1983), two of the most important tasks for humans in automated systems are monitoring the system to make sure it performs according to expectations and to be ready to resume control when the automation deviates from expectation (Stanton & Marsden, 1996). Research has shown that vehicle automation has a negative effect on mental workload and situation awareness (Endsley & Kaber, 1999; Kaber & Endsley, 1997; Stanton et al., 1997; Stanton & Young, 2005; Young & Stanton, 2002), and that reaction times increase as the level of automation increases (Young & Stanton, 2007). This becomes problematic when the driver is expected to regain control when system limits are exceeded, as a result of a sudden automation failure. Failure-induced transfer of control has been extensively studied (see Desmond et al., 1998; Molloy & Parasuraman, 1996; Stanton et al., 1997; Stanton et al., 2001; Strand et al., 2014; Young & Stanton, 2007). In one failure-induced control-transition-scenario, Stanton et al. (1997) found that more than a third of drivers failed to regain control of the vehicle following an automation failure whilst using Adaptive Cruise Control. Other research has shown that it takes approximately one second for a driver manually driving to respond to an unexpected and sudden braking event in traffic (Summala, 2000; Swaroop & Rajagopal, 2001; Wolterink et al., 2011). Young and Stanton (2007) report brake reaction times of 2.13±0.55 seconds for drivers using Adaptive Cruise Control (SAE Level 1), and brake reaction times of 2.48±0.66 seconds for drivers with Adaptive Cruise Control and Assistive Steering (SAE Level 2). By contrasting the results from Young and Stanton (2007) where drivers experienced an automation failure whilst a lead vehicle suddenly braked, with Summala (2000) it seems like it takes an additional 1.1-1.5 seconds to react to sudden events requiring braking whilst driving with Driver Assistance Automation (SAE Level 1) and Partial Driving Automation (SAE Level 2). This increase, in combination with headways as short as 0.3 seconds (Willemsen et al., 2015) coupled with evidence that drivers are poor monitors (Molloy & Parasuraman, 1996), could actually cause accidents. Evidently, automating the driving task seem to have a detrimental effect on driver reaction time (Young & Stanton, 2007). Therefore, as Cranor (2008) and Eriksson and Stanton (2016) proposed, the driver needs to receive appropriate feedback if they are to successfully re-enter the driving control loop. Recent research efforts have been made to determine the optimal Take-Over-Request lead time (TORlt: the lead-time from a ‘take-over request’ (TOR) to a critical event, such as a stranded vehicle) and Take Over reaction time (TOrt: the time is takes the driver to take back control of the vehicle from the automated system when a TOR has been issued) with times varying from 0-30 seconds for TORlt  and 1.14-15 seconds for TOrt as shown in Table 1. A total of 25 papers reported either TORlt, or TOrt and were included in the review (see Table 1).

Table 1. Papers included in the review. Modalities for the Take-over request is coded as: A = Auditory, V = Visual, H = Haptic and B = Brake Jerk.

| Paper | TORlt | TOrt | Modality |
| --- | --- | --- | --- |
| 1 | Gold et al. (2016) | 7 | 2.47-3.61 | - |
| 2 | Körber et al. (2015) | 3 | - | A |
| 3 | Louw et al. (2015b) | 6.5 | 2.18-2.47 | A |
| 4 | Zeeb et al. (2016) | 2.5, 4 | - | V |
| 5 | Damböck et al. (2012) | 4, 6, 8 | - | A |
| 6 | Kerschbaum et al. (2015) | 7 | 2.22-3.09 | V A |
| 7 | Belderbos (2015) | 10 | 5.86-5.87 | V A H |
| 8 | Walch et al. (2015) | 4, 6 | 1.90-2.75 | V A |
| 9 | Lorenz et al. (2014) | 7 | 2.86-3.03 | V A |
| 10 | Merat et al. (2014) | 0 | 10-15 | - |
| 11 | Naujoks et al. (2014) | - | 2.29-6.90 | V A |
| 12 | Schömig et al. (2015) | 12 | - | V A |
| 13 | Louw et al. (2015a) | 3 | - | V A |
| 14 | Zeeb et al. (2015) | 2.5, 3, 3.5, 12 | 1.14 | V A |
| 15 | Mok et al. (2015) | 2, 5, 8 | - | A |
| 16 | Gold et al. (2014) | 5 | 1.67-2.22 | V A |
| 17 | Radlmayr et al. (2014) | 7 | 1.55-2.92 | V A |
| 18 | Dogan et al. (2014) | 3 | - | V A |
| 19 | Gold et al. (2013) | 5, 7 | 2.06-3.65 | V A |
| 20 | van den Beukel and van der Voort (2013) | 1.5, 2.2, 2.8 | - | A |
| 21 | Melcher et al. (2015) | 10 | 3.42-3.77 | V A B |
| 22 | Naujoks and Nekum (2014) | 0, 1, 2, 3, 4 | - | V A |
| 23 | Feldhütter et al. (2016) | 6 | 1.88-2.24 | A |
| 24 | Payre et al. (2016) | 2, 30 | 4.30-8.70 | V A |
| 25 | Körber et al. (2016) | 7 | 2.41-3.66 | A |

The review showed that the mean TORlt was 6.37±5.36 seconds (Figure 1) with a mean reaction time of 2.96±1.96 seconds. The most frequently used TORlts tended to be; 3 seconds with a mean TOrt of 1.14±0.45 [studies 2, 13, 14, 18, 22], 4 seconds with a mean TOrt of 2.05±0.13 [studies 4, 8, 22], 6 seconds with a mean TOrt of 2.69±2.21 [studies 5, 8, 23], and 7 seconds with a mean TOrt of 3.04±1.6 [studies 1, 6, 9, 17, 19, 25] as shown in Figure 2.

Figure 1. The TORlt used in the reviewed papers. Several papers used a multitude of TOR lead times and thus contributed on several points of the graph.

Take Over reaction times stay fairly consistent around 2-3.5 seconds in most control transitions, with a few outliers, as seen in Figure 2. Belderbos (2015), Merat et al. (2014), Naujoks et al. (2014) and Payre et al. (2016) show longer TOrt compared to the rest of the reviewed papers. Merat et al. (2014) and Naujoks et al. (2014) had the control transition initiated without any lead time whereas Belderbos (2015) and Payre et al. (2016) did. Merat et al. (2014) showed that there is a 10-15 second time lag between the disengagement of the automated driving system and resumption of control by the driver. Notably, the control transition was system initiated and lacked a pre-emptive TOR which may have caused the increase in TOrt. Similarly, Naujoks et al. (2014) observed a 6.9 second TOrt from when a TOR was issued and the automation disconnected until the driver resumed control in situations where automation became unavailable due to missing line markings, the beginning of a work zone or entering a curve. Based on personal communication with the author, the vehicle would have crossed the lane markings after approximately 13 seconds, and would have reached the faded lane markings approximately 10 seconds after the TOR. The velocity in Naujoks et al. (2014) was 50 Kph, which is fairly slow compared to most other TOR studies that use speeds over 100 Kph [studies 1, 3, 4, 6, 9, 10, 12, 14, 17, 19, 21, 23, 24, 25] and may have had an effect on the perceived urgency.

Figure 2. Take Over reaction time averages for all the conditions in the reviewed studies. Some studies had more than one take over event and is therefore featured multiple times.

Belderbos (2015) showed TOrt’s of 5.86±1.57 to 5.87±4.01 when drivers were given a TORlt of 10 seconds during unsupervised automated driving. Payre et al. (2016) utilised two different TORlt’s, 2, and 30 seconds. These TORlt’s produced significant differences in TOrt, the 2 second TORlt produced a TOrt of 4.3±1.2 seconds and the two scenarios that used the 30 second TORlt produced TOrt’s of 8.7±2.7 seconds and 6.8±2.5 seconds respectively. The shorter TOrt of the two 30 second TOR events occurred after the 2 second emergency TOR and could have been affected by the urgency caused by the short lead time in the preceding, shorter TOR.

Merat et al. (2014) concluded, based on their observed TOrt, that there is a need for a timely and appropriate notification of an imminent control transition. This observation is in line with the current SAE-guidelines which state that the driver “Is receptive to a request to intervene and responds by performing dynamic driving task fallback in a timely manner”(SAE International, 2016, p. 20). In initial efforts to determine how long in advance the driver needs to be notified before a control transition is initiated, Damböck et al. (2012) and Gold et al. (2013) explored a set of TOR lead times. Damböck et al. (2012) utilised three TORlt’s, 4, 6, and 8 seconds and found that given an 8 second lead time, drivers did not differ significantly from manual driving. This was confirmed by Gold et al. (2013) who reported that drivers need to be warned at least 7 seconds in advance of a control transition to safely resume control. These findings seem to have been the inspiration for the TORlt of some recent work utilising timings around 7 seconds [studies 1, 6, 9, 17].

A caveat of a number of the reviewed studies is that the lead time given in certain scenarios such as; disappearing lane markings, construction zones, and merging motorway lanes is surprisingly short, from 0 to 12 seconds (c.f. Table 1), and will likely be longer in on road use cases [studies 4, 5, 11, 14, 15, 21]. The reason for this is the increasing accuracy of contemporary GPS hardware and associated services, such as Google Maps. Such services are already able to direct lane positioning whilst driving manually, as well as notifying drivers of construction zones and alternate, faster routes. Thus, there is no evident gain of having short lead times in such situations.

Several of the studies reviewed have explored the effect of TOR’s in different critical settings by issuing the TOR immediately preceding a time critical event [studies 1, 2, 3, 4, 6, 7, 8, 9, 13, 16, 17, 19, 20, 23, 24, 25]. These studies have explored how drivers manage critical situations in terms of driving behaviour, workload, and scanning behaviour. Whilst it is of utmost importance to know how quickly a driver can respond to a TOR and what the shortest TOR-times are in emergencies, there is a paucity of research exploring the time it takes a driver to resume control in normal, non-critical, situations. We argue that if the design of normal, non-critical, control transitions are designed based on data obtained in studies utilising critical situations, there is a risk of unwanted consequences such as: drivers not responding optimally due to too short lead time (suboptimal responses are acceptable in emergencies as drivers are tasked with avoiding danger), drivers being unable to fully regain situation awareness, and sudden, dramatic, increases in workload. Arguably, these consequences should not be present in every transition of control as it poses a safety risk for the driver, as well as other road users. Therefore, the aim of this study is to establish driver take-over time in normal traffic situations when, e.g. the vehicle is leaving its Operational Design Domain as these will account for most of the situations (Nilsson, 2014; SAE International, 2016). We also explore how TOR take-over time is affected by a non-driving secondary task, as this was expected to increase the reaction time (Merat et al., 2012).

Moreover, none of the papers included in the review mentioned the time it takes drivers to transition from manual to automated driving. Gaining an understanding on the time required to toggle an automated driving system on is important in situations such as: entering an area dedicated to automated vehicles or engaging the automated driving mode in preparation for joining a platoon as proposed by the SARTRE project (Robinson et al., 2010). Therefore, the aim of this study was to establish the time it takes a driver to switch to automated driving when automated driving features become available. Ultimately, this research aims to provide guidance about the lead-time required to get the driver back into, and out of, the manual vehicle control loop.

Method

Participants

Twenty-six participants (10 females, 16 males) between 20 and 52 years of age (M = 30.27 SD = 8.52) with a minimum one year and an average 10.57 years (SD = 8.61) of driving experience were asked to take part in the trial. Upon recruiting participants, their informed consent was obtained. The study complied with the American Psychological Association Code of Ethics and had been approved by the University of Southampton Ethics Research and Governance Office (ERGO number 17771).

Equipment

The experiment was carried out in a fixed based driving simulator located at the University of Southampton. The simulator was a Jaguar XJ 350 with pedal and steering sensors provided by Systems Technology Inc. as part of STISIM Drive® M500W Version 3 (http://www.stisimdrive.com/m500w) providing a projected 140° field of view. Rear view- and side-mirrors were provided through additional projectors and video cameras. The original Jaguar XJ instrument cluster was replaced with a 10.6” Sharp LQ106K1LA01B Laptop LCD panel connected to the computer via a RTMC1B LCD controller board to display computer generated graphics components for TOR’s. The default configuration of the instrument cluster is shown in Figure 3.

Figure 3. The instrument cluster in its default configuration

When a TOR was issued the engine speed dial was hidden and the request was shown in its place. The symbol asking for control resumption is shown in Figure 5 and the symbol used to prompt the driver to re-engage the automation is shown in Figure 4.

Figure 4. The icon shown when the automation becomes available. The icon was coupled with a computer generated voice message stating “automation available”.

Figure 5. The take-over request icon shown on the instrument cluster. The icon was coupled with a computer generated voice message stating "please resume control”.

The mode switching human machine interface was located on a Windows tablet in the centre console, consisting of two buttons, used either to engage, or to disengage the automation. To enable dynamic dis-engagement and re-engagement of the automation, bespoke algorithms were developed and are reported elsewhere (c.f. Eriksson et al., 2016).

Experiment Design

The experiment had a repeated-measures, within-subject design with three conditions; Manual, Highly Automated Driving (HAD) and Highly Automated Driving with a secondary task. The conditions were counterbalanced to counteract order effects. For the automated conditions, participants drove at 70 mph on a 30 kilometre, three lane highway with some curves, with oncoming traffic in the opposing three lanes separated by a barrier and moderate traffic conditions. The route was mirrored between the two automated conditions to reduce familiarity effects whilst keeping the roadway layout consistent.

In the secondary task condition, drivers were asked to read (in their head) an issue of National Geographic whilst the automated driving system was engaged in order to remove them from the driving (and monitoring) task. During both conditions, drivers were prompted to either resume control from, or relinquish control to, the automated driving system. The control transition requests were presented as both a visual cue (c.f. Figure 4 and Figure 5) and an auditory message, in line with previous research [studies 6,7,8,9,11,12,13,14,16,17,18,19,22,24], in the form of a computer generated, female voice stating “please resume control” or “automation available”. No haptic feedback was included in this study, despite the findings from Petermeijer et al. (2016) and Scott and Gray (2008) showing shorter reaction times when vibrotactile feedback was used. The motivation for excluding the haptic modality was that it was under-represented in the review, with only 1 paper in the review utilising a form of haptic feedback. Furthermore, Petermeijer et al. (2016) concluded that haptic feedback is best suited for warnings, and as the current experimental design explored non-critical warnings, no motivation for including haptics could be found.  The interval in which these requests were issued ranged from 30-45 seconds, thus allowing for approximately 24 control transitions of which half were to manual control.

Procedure

Upon arrival, participants were asked to read an information sheet, containing information regarding the study, the right to at any point abort their trial without any questions asked. After reading the information sheet the participants were asked to sign an informed consent form. They were also told that they were able to override any system inputs via the steering wheel, throttle or brake pedals. Drivers were reminded that they were responsible for the safe operation of the vehicle regardless of its mode (manual or automated), and thus needed to be able to safely resume control in case of failure. This is in accordance with current legislation (United Nations, 1968) and recent amendments to the Vienna Convention of Road Traffic. They were informed that the system may prompt them to either resume or relinquish control of the vehicle, and that when such a prompt was issued they were required to adhere to the instruction, but only when they felt safe doing so. This instruction was intended to reduce the pressure on drivers to respond immediately and to reinforce the idea that they were ultimately responsible for safe vehicle operation.

At the end of each driving condition, participants were asked to fill out the NASA-RTLX (Byers et al., 1989). They were also offered a short break before continuing the study. Reaction time data were logged for each transition to and from manual control.

Dependent variables

The following metrics were collected for each condition per participant.

Reaction time to the control transition request was recorded from the onset of the TOR. The control transition request was presented in the instrument cluster coupled with a computer generated voice to initiate a change in mode to and from manual control and was recorded in milliseconds.

Driving performance as measured by Standard Deviation of Steering Angular rate (degrees / second).

Subjective workload scores were collected via the NASA-TLX sub-scales at the end of each driving condition. Overall workload score was calculated through the summation of sub-scales (Byers et al., 1989; Hart & Staveland, 1988).

Analysis

The dependent measures were tested for normal distribution using the Kolmogorov-Smirnov test, which revealed that the data was non-normally distributed. To assess driving performance after control was handed back to the driver, a measure of the standard deviation of the absolute steering angular rate was used to capture corrective steering actions  (Fisher et al., 2011 ch 40, pp 10). Furthermore, as the TOrt data is reaction time data, the median TOrt values for each participant was calculated after which Wilcoxon signed-rank test was used to analyse the time and workload data. The box plots in Figure 6 and Figure 8 had their outlier thresholds adjusted to accommodate the log-normal distribution of the TOrt data by using the LIBRA library for MatLab (Verboven & Hubert, 2005) and its method for robust boxplots for non-normally distributed data by Hubert and Vandervieren (2008). Effect sizes were calculated as: r = abs(Z/√N).

Results

The results showed that it took approximately 4.2-4.4±1.96-1.80 seconds (median) to switch to automated driving, see Table 2. No significant differences between the two conditions could be found when drivers transitioned from manual to automated driving (Z = -0.673, p = 0.5, r = 0.13). Control transition times from manual to automated driving in the two conditions is shown in Figure 6 and individual transition times for each participant are available in the supplementary material.

Figure 6. Adjusted box-plot of control transition times from manual driving to Automated Driving. The dashed horizontal line indicates the max/min values assuming a normal distribution.

Figure 7. A distribution plot of TOrt when drivers were prompted to engage the automation. The asterisk* marks the median value, the X axis contains 160 bins.

The results showed a significant increase in control transition time of ~1.5 seconds when drivers were prompted to resume control whilst engaged in a secondary task (Z = -4.43, p < 0.01, r = 0.86). It took drivers approximately 4.46±1.63 seconds to resume control when not occupied by a secondary task, and 6.06±2.39 seconds to resume control when engaged in a secondary task as shown in Table 2.

Table 2. Descriptive statistics of the control transition times (in milliseconds) from Automated Driving to manual control, and from manual control to Automated Driving as well as descriptive statistics from the presented TOrt’s from the reviewed articles.

|  | Meta-review | From Automated to Manual | From Manual to Automated |
| --- | --- | --- | --- |
|  |  | No secondary task | Secondary task | No secondary task | Secondary task |
| Median | 2470 ms | 4567 ms | 6061 ms | 4200 ms | 4408 ms |
| IQR | 1415 ms | 1632 ms | 2393 ms | 1964 ms | 1800 ms |
| Min | 1140 ms | 1975 ms | 3179 ms | 2822 ms | 2926 ms |
| Max | 15000 ms | 25750 ms | 20994 ms | 23884 ms | 23221 ms |

Figure 8. Adjusted boxplot of the Take Over reaction time when switching from automated to manual control in the two experimental conditions contrasted with the TOrt of the reviewed papers.

Figure 9 A distribution plot of TOrt when drivers were prompted to resume manual control. The asterisk* marks the median value, the X axis contains 160 bins. The amplitude of the reviewed papers is caused by the low number of values provided by the reviewed papers.

The results from analysing the driving performance data from 0 to 18 seconds post control transition showed non-significant differences in Standard Deviation of Absolute Steering Angular Rate (Table 3) between the two task conditions.

Table 3. Standard deviation of Angular Rate (Degrees/second) for the two task conditions from 0-18 seconds post take-over.

|  |  | No secondary task | With secondary task |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | time | M (SD) | M (SD) | Z | p | r |
|  | 0-3s | 0.08 (0.06) | 0.08 (0.06) | -0.11 | 0.91 | 0.02 |
|  | 3-6s | 0.03 (0.03) | 0.03 (0.03) | -0.14 | 0.89 | 0.03 |
|  | 6-9s | 0.02 (0.02) | 0.06 (0.17) | -1.48 | 0.13 | 0.29 |
|  | 9-12s | 0.02 (0.02) | 0.11 (0.44) | -0.98 | 0.33 | 0.19 |
|  | 12-15s | 0.02 (0.02) | 0.11 (0.45) | -0.39 | 0.69 | 0.08 |
|  | 15-18s | 0.03 (0.07) | 0.13 (0.51) | -0.42 | 0.67 | 0.08 |

The analysis of the subjective ratings for driver mental workload showed that the secondary task condition has marginally higher scores overall, as shown in Table 4. Only temporal demand had a statistically significant difference (Z= -3.11, p < 0.05, r = 0.61), with higher rated demand in the secondary task condition as shown in Figure 10.

Table 4. Overall workload scores as well as individual workload ratings for the two conditions. ** = Significant at the 0.01 level.

|  |  | Without secondary task | With secondary task |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Variable |  | Median (IQR) | Median (IQR) | Z | p | r |
| Overall Workload | 5 (7.33) | 6.2 (6.5) | -1.953 | 0.051 | 0.38 |
| Mental demand | 7.5 (10) | 10.5 (9) | -1.41 | 0.16 | 0.28 |
| Physical demand | 4 (5) | 5.5 (6) | -1.93 | 0.054 | 0.38 |
| Temporal demand | 3 (6) | 8.5 (8) | -3.11 | 0.00** | 0.61 |
| Performance | 6 (7) | 4.5 (5) | -0.47 | 0.63 | 0.09 |
| Effort | 5 (9) | 7 (8) | -0.23 | 0.82 | 0.05 |
| Frustration | 4 (9) | 6.5 (7) | -1.04 | 0.3 | 0.2 |

Figure 10. Boxplot of Subjective estimations of workload in the two conditions.

Discussion

Relinquishing control to automation

In this study we subjected drivers to multiple control transitions between manual and automated control in a highway scenario. Upon reviewing the literature, no mention of how long the driver takes to engage an automated driving system was found, making this study a first-of-a-kind. We found that drivers take between 2.82-23.8 seconds (Median = 4.2-4.4) to engage automated driving when the system indicates that the feature is available. No significant differences between the two conditions was found, but as Figure 6 shows, there was large range in the time it takes to relinquish control. It is clear from Figure 7 that designing for the median, or average driver effectively exclude a large part of the user group, which could have severe implications for drivers who fall outside of the mean or median. It has been common practice in Human Factors and Anthropometrics to design for 90% of the population, normally through accommodating the range between the 5th percentile female and the 95th percentile male (Porter et al., 2004). Thus, it is important that vehicle manufacturers are made aware of the intra-individual differences, as such differences have a large effect on the larger traffic system if drivers are expected to toggle Automated Driving systems within a certain time frame. An example of potential situations where the driver would need to toggle the automated driving system could be in HAD-dedicated areas. Moreover, it may be that the time it takes to engage the automated driving system depends on external factors such as, perceived safety, weather conditions, traffic flow rates, presence of vulnerable road users, roadworks, and so on. If the driver deems a situation unsafe, or has doubts as to how well the automation would perform in a situation, the driver may hold off on completing a transition until the driver feels that the system can comfortably handle the situation.

Resuming control from automation

Previous research was reviewed and it was found that most studies utilised system paced transitions, where the automated driving system warns in advance of failure or reduced automation support with relatively short lead times, from 3 seconds [studies 2, 13, 14, 18, 22] to 7 seconds [studies 1, 6, 9, 17, 19, 25]. It has previously been shown that whilst it takes approximately 2.47±1.42 seconds on average, it can take up to 15 seconds to respond to such an event (Merat et al., 2014). We argue that this use case, albeit important, does not reflect the primary use case for control transitions in highly automated driving. When comparing the range of TOrt in the literature to the user paced (no secondary task) condition in this study, a great deal of overlap can be seen. The observed values in the current study are closer to the higher values observed by Merat et al. (2014) whilst the median range of 4.56-6.06s is closer to the range of times suggested by Gold et al. (2013) and Damböck et al. (2012). It is evident that there is a large spread in the TOrt, which when designing driving automation should be considered, as the range of performance is more important than the median or mean, as these exclude a large portion of drivers.

When subjecting drivers to TOR’s without time restrictions we found that drivers take between 1.97-25.75 seconds (Median = 4.56) to resume control from automated driving in normal conditions, and between 3.17-20.99 seconds (Median = 6.06) to do so whilst engaged in a secondary task preceding the control transition. This shows that there is a median 2 second difference in control transition times in the reviewed manuscripts compared to the user paced control transitions. There was a large effect of secondary task engagement on TOrt, showing an increase in driver control resumption times when engaged in a secondary task. This might be explained in part by the nature of the secondary task, as the driver had to allocate time to put down the magazine they were asked to read whilst the automated driving feature was activated. It could also be partly attributed to driver task adaptation, by holding off transferring control until they have had time to switch between the reading task and driving task. This is supported by research indicating that drivers tend to adapt to external factors such as traffic complexity to allow for more time to make decisions (Eriksson et al., 2014), by for example slowing down when engaged in secondary tasks (Cooper et al., 2009) or the expectation of resuming control (Young & Stanton, 2007). In light of these results, there is a case for “adaptive automation” that modulates TORlt by, for example, detecting whether the driver gaze is off road for a certain time-period, providing the driver with a few additional seconds before resuming control.

Furthermore, the 1.5 second increase of control resumption time when engaged in a reading task is similar to the reaction time increase caused by the introduction of automated driving features observed by Young and Stanton (2007) compared to reaction time in manual driving (Summala, 2000). Therefore, a further increase of reaction times when drivers are engaged in other tasks will have to be expected, but measures must be taken to reduce the increase in reaction time, for example through the addition of informative displays, to reduce the risk of accidents (Cranor, 2008; Eriksson & Stanton, 2016).

There was a significant increase in perceived temporal demand when drivers were tasked with reading whilst the automation was engaged. This increase in perceived temporal demand may have been caused by the TOR, and the driver not being fully sure as to how long the vehicle could manage before a forced transition would occur (this was not a possibility in the current experiment). This increase in perceived temporal demand could also be attributed to the pace of the experiment, and that the drivers were required to pick up, and put down the magazine whenever a control transition was issued. Overall there are little differences in workload, and the median workload in both conditions was approximately at the halfway point on the scale, implying optimal loading (Stanton et al., 2011).

In light of these results, combined with the non-significant, small effect of task condition on driving performance indicated that the drivers were able to self-regulate the control transition process by adapting the time needed to resume control (Eriksson et al., 2014; Kircher et al., 2014) and therefore maintaining optimal levels of workload, minimizing the severity of the after-effects observed in studies by e.g. Gold et al. (2013).

Conclusions

Relinquishing control to automation

The literature on control transitions in highly automated driving is absent in research reports on transitions from manual to automated vehicle control. In a first-of-a-kind study, we found that it takes drivers between 2.8 and 23.8 seconds to switch from manual to automated control. This finding has some implications for the safety of drivers merging into automated driving dedicated lanes, or other infrastructure whilst in manual mode. Such an event may require certain adaptations for traffic already occupying such a lane. Adaptations may include increasing time-headway or reducing speed to accommodate the natural variance in human behaviour to avoid collisions, or discomfort for road users in such a lane. Moreover, it may be that part of the variance could be reduced by designing merging zones on straight, uncomplicated road sections as drivers may otherwise hold off transferring control to the automated driving system until the driver feels it safe to hand control to the automated driving system.

Resuming control from automation

A review of the literature found that most papers tend to report the mean Take Over reaction time and often fail to report standard deviation and range (c.f. Figure 2), thus the variance in control transition times remain unknown (median, and interquartile range for each participant in this study can be found in the supplementary material). Additionally, the reviewed papers tended to give drivers a lead time of between 0 and 30 seconds between the presentation of a TOR and a critical event with the main part of the reviewed papers using a 3 or 7 second lead time. In this study we found that the range of time in which drivers resume control from the automated driving system was between 1.9 and 25.7 seconds depending on task engagement. The spread of TOrt in the two conditions in this study indicates that mean, or median values do not tell the entire story when it comes to control transitions. Notably, the distribution of TOrt approaches platykurtic (c.f. Figure 9) when drivers are engaged in a secondary task. This implies that vehicle manufacturers must adapt to the circumstances, providing more time to drivers who are engaged in secondary tasks, whilst in highly automated driving mode to avoid excluding drivers at the tail of the distribution. In light of this, designers of automated vehicles should not focus on the mean, or median, driver when it comes to control transition times. Rather they should strive to include the larger range of control transitions times so they do not exclude users that fall outside the mean or median. Moreover, policy-makers should strive to accommodate these inter- and intra-individual differences in their guidelines for “sufficiently comfortable transition times”.  When drivers were allowed to self-regulate the control transition process, little differences could be found in both driving performance and workload between the two conditions. This lends further support to the argument for designing for the range of transition-times rather than the mean or median in non-critical situations.

Lastly, based on the large decrease in TOrt kurtosis when drivers were engaged in a secondary task, it may also be the case that future automated vehicles need to adapt the TORlt to account for drivers engaged in other, non-driving, tasks and even adapt TORlt to accommodate external factors such as traffic density and weather.

Key Points

- Large differences between control transitions times reported in the literature and the no-secondary task condition were found.

- Drivers take longer to resume control from automation when engaged in a secondary task prior to the control transition.

An inclusive design approach is needed to accommodate the observed variance as the mean or median response times are not sufficient when it comes to designing control transitions in automated driving.

References

Audi. (2014). Audi piloted driving. from http://www.audi.com/com/brand/en/vorsprung_durch_technik/content/2014/10/piloted-driving.html

Bainbridge, L. (1983). Ironies of Automation. Automatica, vol 19, no 6, pp 775-779.

Banks, V. A., & Stanton, N. A. (2015). Contrasting models of driver behaviour in emergencies using retrospective verbalisations and network analysis. Ergonomics, vol 58, no 8, pp 1337-1346.

Banks, V. A., & Stanton, N. A. (2016). Keep the driver in control: Automating automobiles of the future. Appl Ergon, vol 53 Pt B, pp 389-395.

Belderbos, C. (2015). Authority Transition Interface: A Human Machine Interface for Taking over Control from a Highly Automated Truck. TU Delft, Delft University of Technology.

BMW. (2013). ConnectedDrive.

Byers, J. C., Bittner, A., & Hill, S. (1989). Traditional and raw task load index (TLX) correlations: Are paired comparisons necessary. Advances in industrial ergonomics and safety I, pp 481-485.

Cooper, J. M., Vladisavljevic, I., Medeiros-Ward, N., Martin, P. T., & Strayer, D. L. (2009). An investigation of driver distraction near the tipping point of traffic flow stability. Human Factors: The Journal of the Human Factors and Ergonomics Society, vol 51, no 2, pp 261-268.

Cranor, L. F. (2008). A framework for reasoning about the human in the loop. Paper presented at the Proceedings of the 1st Conference on Usability, Psychology, and Security.

Damböck, D., Bengler, K., Farid, M., & Tönert, L. (2012). Übernahmezeiten beim hochautomatisierten Fahren. Tagung Fahrerassistenz. München, vol 15, pp 16.

Desmond, P. A., Hancock, P. A., & Monette, J. L. (1998). Fatigue and automation-induced impairments in simulated driving performance. Human Performance, User Information, and Highway Design, no 1628, pp 8-14.

Dogan, E., Deborne, R., Delhomme, P., Kemeny, A., & Jonville, P. (2014). Evaluating the shift of control between driver and vehicle at high automation at low speed: The role of anticipation. Paper presented at the Transport Research Arena (TRA) 5th Conference: Transport Solutions from Research to Deployment.

Endsley, M. R., & Kaber, D. B. (1999). Level of automation effects on performance, situation awareness and workload in a dynamic control task. Ergonomics, vol 42, no 3, pp 462-492.

Eriksson, A., Lindström, A., Seward, A., Seward, A., & Kircher, K. (2014). Can user-paced, menu-free spoken language interfaces improve dual task handling while driving? Human-Computer Interaction. Advanced Interaction Modalities and Techniques (pp. 394-405): Springer.

Eriksson, A., Spychala, A., F., D. W. J. C., & Stanton, N. A. (2016). A Highly Automated Driving Algorithm Implementation on STISIM. Paper presented at the AHFE 2016.

Eriksson, A., & Stanton, N. A. (2016). The Chatty Co-Driver: A Linguistics Approach to Human-Automation-Interaction. Paper presented at the IEHF2016.

Feldhütter, A., Gold, C., Schneider, S., & Bengler, K. (2016). How the Duration of Automated Driving Influences Take-Over Performance and Gaze Behavior. Paper presented at the Arbeit in komplexen Systemen - Digital, vernetz, human?! 62. Kongress der Gesellschaft für Arbeitswissenschaft.

Fisher, D. L., Rizzo, M., Caird, J., & Lee, J. D. (2011). Handbook of driving simulation for engineering, medicine, and psychology: CRC Press.

Gold, C., Damböck, D., Lorenz, L., & Bengler, K. (2013). “Take over!” How long does it take to get the driver back into the loop? Paper presented at the Proceedings of the Human Factors and Ergonomics Society Annual Meeting.

Gold, C., Korber, M., Lechner, D., & Bengler, K. (2016). Taking Over Control From Highly Automated Vehicles in Complex Traffic Situations: The Role of Traffic Density. Hum Factors.

Gold, C., Lorenz, L., & Bengler, K. (2014). Influence of automated brake application on take-over situations in highly automated driving scenarios. Paper presented at the Proceedings of the FISITA 2014 World Automotive Congress.(in print).

Hart, S. G., & Staveland, L. E. (1988). Development of NASA-TLX (Task Load Index): Results of empirical and theoretical research. Advances in psychology, vol 52, pp 139-183.

Hubert, M., & Vandervieren, E. (2008). An adjusted boxplot for skewed distributions. Computational statistics & data analysis, vol 52, no 12, pp 5186-5201.

Kaber, D. B., & Endsley, M. R. (1997). Out-of-the-loop performance problems and the use of intermediate levels of automation for improved control system functioning and safety. Process Safety Progress, vol 16, no 3, pp 126-131.

Kerschbaum, P., Lorenz, L., & Bengler, K. (2015). A transforming steering wheel for highly automated cars. Paper presented at the Intelligent Vehicles Symposium (IV), 2015 IEEE.

Kircher, K., Larsson, A., & Hultgren, J. A. (2014). Tactical driving behavior with different levels of automation. IEEE Transactions on Intelligent Transportation Systems, vol 15, pp 158-167.

Körber, M., Gold, C., Lechner, D., & Bengler, K. (2016). The influence of age on the take-over of vehicle control in highly automated driving. Transportation Research Part F: Traffic Psychology and Behaviour, vol 39, pp 19-32.

Körber, M., Weißgerber, T., Kalb, L., Blaschke, C., & Farid, M. (2015). Prediction of take-over time in highly automated driving by two psychometric tests. Dyna, vol 82, no 193, pp 195-201.

Lorenz, L., Kerschbaum, P., & Schumann, J. (2014). Designing take over scenarios for automated driving How does augmented reality support the driver to get back into the loop? Paper presented at the Proceedings of the Human Factors and Ergonomics Society Annual Meeting.

Louw, T., Kountouriotis, G., Carsten, O., & Merat, N. (2015a). Driver Inattention During Vehicle Automation: How Does Driver Engagement Affect Resumption Of Control?

Louw, T., Merat, N., & Jamson, H. (2015b). Engaging with Highly Automated Driving: To be or Not to be in the Loop? Paper presented at the 8th International Driving Symposium on Human Factors in Driver Assessment, Training and Vehicle Design, At Salt Lake City, Utah, USA.

Lu, Z., & de Winter, J. C. F. (2015). A Review and Framework of Control Authority Transitions in Automated Driving. Procedia Manufacturing, vol 3, pp 2510-2517.

Melcher, V., Rauh, S., Diederichs, F., Widlroither, H., & Bauer, W. (2015). Take-Over Requests for Automated Driving. Procedia Manufacturing, vol 3, pp 2867-2873.

Merat, N., Jamson, A. H., Lai, F. C., & Carsten, O. (2012). Highly automated driving, secondary task performance, and driver state. Human Factors: The Journal of the Human Factors and Ergonomics Society, vol 54, no 5, pp 762-771.

Merat, N., Jamson, A. H., Lai, F. F. C. H., Daly, M., & Carsten, O. M. J. (2014). Transition to manual: Driver behaviour when resuming control from a highly automated vehicle. Transportation Research Part F: Traffic Psychology and Behaviour, vol 26, Part A, pp 1-9.

Michon, J. A. (1985). A critical view of driver behavior models: What do we know, what should we do? In L. Evans & R. C. Schwing (Eds.), Human behavior and traffic safety. New York: Plenum Press.

Mok, B., Johns, M., Lee, K. J., Miller, D., Sirkin, D., Ive, P., et al. (2015). Emergency, Automation Off: Unstructured Transition Timing for Distracted Drivers of Automated Vehicles. Paper presented at the Intelligent Transportation Systems (ITSC), 2015 IEEE 18th International Conference on.

Molloy, R., & Parasuraman, R. (1996). Monitoring an automated system for a single failure: Vigilance and task complexity effects. Human Factors, vol 38, no 2, pp 311-322.

Naujoks, F., Mai, C., & Nekum, A. (2014, 19-23 July). The effect of urgency of take-over requests during highly automated driving under distracted conditions. Paper presented at the 5th International Conference on Applied Human Factors and Ergonomics AHFE 2014, Krakow, Poland.

Naujoks, F., & Nekum, A. (2014). Timing of in-vehicle advisory warnings based on cooperative perception. Paper presented at the Human Factors and Ergonomics Society Europe Chapter Annual Meeting.

Nilsson, J. (2014). Safe Transitions to Manual Driving From Faulty Automated Driving System: Chalmers University of Technology.

Payre, W., Cestac, J., & Delhomme, P. (2016). Fully Automated Driving: Impact of Trust and Practice on Manual Control Recovery. Hum Factors, vol 58, no 2, pp 229-241.

Petermeijer, S. M., de Winter, J. C. F., & Bengler, K. J. (2016). Vibrotactile Displays: A Survey With a View on Highly Automated Driving. IEEE Transactions on Intelligent Transportation Systems, vol 17, no 4, pp 897-907.

Porter, J. M., Case, K., Marshall, R., Gyi, D., & Sims neé Oliver, R. (2004). ‘Beyond Jack and Jill’: designing for individuals using HADRIAN. International Journal of Industrial Ergonomics, vol 33, no 3, pp 249-264.

Radlmayr, J., Gold, C., Lorenz, L., Farid, M., & Bengler, K. (2014). How Traffic Situations and Non-Driving Related Tasks Affect the Take-Over Quality in Highly Automated Driving. Proceedings of the Human Factors and Ergonomics Society Annual Meeting, vol 58, no 1, pp 2063-2067.

Robinson, T., Chan, E., & Coelingh, E. (2010). Operating platoons on public motorways: An introduction to the sartre platooning programme. Paper presented at the 17th world congress on intelligent transport systems.

SAE International. (2016). Taxonomy and Definitions for Terms Related to Driving Automation Systems for On-Road Motor Vehicles, J3016_201609: SAE International.

safecarnews.com. (2015). Intelligent Drive Concept for new Mercedes-Benz GLC. from http://safecarnews.com/intelligent-drive-concept-for-new-mercedes-benz-glc_ju6145/

Schömig, N., Hargutt, V., Neukum, A., Petermann-Stock, I., & Othersen, I. (2015). The interaction between highly automated driving and the development of drowsiness.

Scott, J., & Gray, R. (2008). A comparison of tactile, visual, and auditory warnings for rear-end collision prevention in simulated driving. Human Factors: The Journal of the Human Factors and Ergonomics Society, vol 50, no 2, pp 264-275.

Stanton, N. A., Dunoyer, A., & Leatherland, A. (2011). Detection of new in-path targets by drivers using Stop & Go Adaptive Cruise Control. Appl Ergon, vol 42, no 4, pp 592-601.

Stanton, N. A., & Marsden, P. (1996). From fly-by-wire to drive-by-wire: Safety implications of automation in vehicles. Safety Science, vol 24, no 1, pp 35-49.

Stanton, N. A., Young, M., & McCaulder, B. (1997). Drive-by-wire: The case of driver workload and reclaiming control with adaptive cruise control. Safety Science, vol 27, no 2-3, pp 149-159.

Stanton, N. A., & Young, M. S. (2005). Driver behaviour with adaptive cruise control. Ergonomics, vol 48, no 10, pp 1294-1313.

Stanton, N. A., Young, M. S., Walker, G. H., Turner, H., & Randle, S. (2001). Automating the Driver’s Control Tasks. INTERNATIONAL JOURNAL OF COGNITIVE ERGONOMICS.

Strand, N., Nilsson, J., Karlsson, I. C. M., & Nilsson, L. (2014). Semi-automated versus highly automated driving in critical situations caused by automation failures. Transportation Research Part F: Traffic Psychology and Behaviour.

Summala, H. (2000). Brake Reaction Times and Driver Behavior Analysis. Transportation Human Factors, vol 2, no 3, pp 217-226.

Swaroop, D., & Rajagopal, K. R. (2001). A review of Constant Time Headway Policy for Automatic Vehicle Following. Paper presented at the IEEE Intelligent Transportation Systems Conference Proceedings, Oakland (CA), USA.

United Nations. (1968). Convention on road traffic, Done at Vienna on 8 November 1968. Amendment 1. Retrieved from http://www.unece.org/fileadmin/DAM/trans/conventn/crt1968e.pdf.

van den Beukel, A. P., & van der Voort, M. C. (2013). The influence of time-criticality on Situation Awareness when retrieving human control after automated driving. Paper presented at the Intelligent Transportation Systems-(ITSC), 2013 16th International IEEE Conference on.

Verboven, S., & Hubert, M. (2005). LIBRA: a MATLAB library for robust analysis. Chemometrics and intelligent laboratory systems, vol 75, no 2, pp 127-136.

Walch, M., Lange, K., Baumann, M., & Weber, M. (2015). Autonomous driving: investigating the feasibility of car-driver handover assistance. Paper presented at the Proceedings of the 7th International Conference on Automotive User Interfaces and Interactive Vehicular Applications.

Walker, G. H., Stanton, N. A., & Salmon, P. M. (2015). Human Factors in Automotive Engineering and Technology: Ashgate: Aldershot.

Willemsen, D., Stuiver, A., & Hogema, J. (2015). Automated Driving Functions Giving Control Back to the Driver: A Simulator Study on Driver State Dependent Strategies. Paper presented at the 24th International Technical Conference on the Enhanced Safety of Vehicles (ESV).

Wolterink, W. K., Heijenk, G., & Karagiannis, G. (2011). Automated Merging in a Cooperative Adaptive Cruise Control (CACC) System. Paper presented at the Fifth ERCIM Workshop on eMobility, Vilanova i la Geltrú, Catalonia, Spain.

Young, M. S., & Stanton, N. A. (2002). Malleable attentional resources theory: a new explanation for the effects of mental underload on performance. Hum Factors, vol 44, no 3, pp 365-375.

Young, M. S., & Stanton, N. A. (2007). Back to the future: brake reaction times for manual and automated vehicles. Ergonomics, vol 50, no 1, pp 46-58.

Zeeb, K., Buchner, A., & Schrauf, M. (2015). What determines the take-over time? An integrated model approach of driver take-over after automated driving. Accident Analysis & Prevention, vol 78, pp 212-221.

Zeeb, K., Buchner, A., & Schrauf, M. (2016). Is take-over time all that matters? The impact of visual-cognitive load on driver take-over quality after conditionally automated driving. Accid Anal Prev, vol 92, pp 230-239.